## Slide 1: Introduction to the Arduino
Ryan Brock

## Slide 2: About Me
Ryan Brock
Software Engineer – 14 Years
Purdue University – Computer Science
Motorola
Zebra Technologies

## Slide 3: Contact
Twitter: @borq79
Email: borq79@gmail.com
Github Repo:
  https://github.com/borq79/Cary-Area-Public-Library-Classes

## Slide 4: Agenda
Intro (5 Minutes)
Quick Basics (15 Minutes)
Project 1 (15 Minutes)
  Bring and LED to life
So What Just Happened? (15 Minutes)
  Basic Circuit
  What is an LED
  Voltage / Current / Resistance
Project 2 (20 Minutes)
  Introducing a button into the circuit
Project 3 (15 Minutes)
  Reading the Temperature of the Room
Project 4 (25 Minutes)
  Multicolor LEDs

## Slide 5: Your Kits
$55 Vilros Ultimate Starter Kit
https://www.vilros.com/ultimate-starter-kit.html
$3 DHT11 Humidity and Temperature Sensor
http://www.dxsoul.com/product/arduino-digital-temperature-humidity-sensor-module-901121350#.V0IP45MrJMP
$8 LED Strip
http://www.amazon.com/NulSom-NeoPixel-Rainbow-Stick-Arduino/dp/B00PTEP14W/ref=sr_1_1?ie=UTF8&qid=1452991973&sr=8-1&keywords=neopixel+stick
$3 20 pc. Capacitor Pack
http://www.dx.com/p/16v-1000uf-aluminum-motherboard-capacitors-20-piece-pack-127865#.V0IQv5MrJMM

## Slide 6: Breadboard
Where is C:19?

## Slide 7: Just Like Battleship

## Slide 8: Wiring up a Circuit

## Slide 9: Project 1 Parts List
Arduino
Breadboard
USB Cable
3 Male-Male wires
1 330 Ohm resistor
1 LED

## Slide 10: Step 1 – Wire up the Rails
Run wire from GND pin on Arduino to Blue Row on Breadboard (green wire in example)
Run wire from 5V pin on Arduino to Red Row on Breadboard (red wire in example)

## Slide 11: Step 2 – Place Resistor
Run wire from the blue row to A:16 (yellow wire in example)
Place one leg of resistor in the red row and the other in I:16

## Slide 12: Step 3 – Place LED
Place the longer leg of the LED into F:16
Place the shorter leg of the LED into E:16

## Slide 13: Step 4 – Apply Power
Plug the Arduino into the USB Cable
Plug the USB Cable into the PC

## Slide 14: So What Just Happened?
Complete Circuit
Arduino acted like a battery
Resistor restricted current flow so LED isn’t damaged

## Slide 15: Water Analogy

## Slide 16: LEDs

## Slide 17: Why is one lead longer?

## Slide 18: Project 2 Parts List
Arduino
Breadboard
USB Cable
3 Male-Male wires
1 330 Ohm resistor
1 LED
1 Button

## Slide 19: Step 1 – Move the Wires
Make sure the USB Cable is not plugged into the PC
Move the wire plugged into GND on the Arudino from the blue row to J:25 on the breadboard (green wire in the example)
Move the wire plugged into 16:A from the blue row to A:25 (yellow wire in the example)

## Slide 20: Step 2 – Place the Button
Place the button across the gap

## Slide 21: Step 3 – Apply Power
Plug the Arduino into the USB Cable
Plug the USB Cable into the PC

## Slide 22: Button as a Switch

## Slide 23: Project 3 - Let’s ’Read’ Something
The Arduino can ‘drive’ pins
The Arduino can also ‘read’ pins
Allows Arduino to ’read’ sensors, collect data, etc.
Need to program the Arduino to make it ‘smart’
The Arduino can set pins to HIGH or LOW
The Arduino can read pins as either HIGH or LOW

## Slide 24: Project 3 Parts List
Arduino
Breadboard
USB Cable
1 DHT11 Humidity / Temperature Sensor
3 Male-Female wires

## Slide 25: Step 1 - Wiring
Make sure the USB Cable is not plugged into the PC
Place a Male-Female connector running from the GND pin of the Arduino to the negative pin of the DHT11 (black wire in example)
Place a Male-Female connector running from the 5V pin of the Arduino to the middle pin of the DHT11 (red wire in example)
Place a Male-Female connector running from the 2 pin of the Arduino to the ‘S pin of the DHT11 (blue wire in example)

## Slide 26: Step 2 – Power the Arduino
Plug the Arduino into the USB Cable
Plug the USB Cable into the PC

## Slide 27: Step 3 – Program the Arduino
Open Sketch dht11.ino in the dht11 directory/folder
Select Tools -> Port
Click the Upload Button

## Slide 28: Step 4 – Open the Serial Monitor
Go to Tools and select ‘Serial Monitor’

## Slide 29: WS2811

## Slide 30: Project 4 Parts List
Arduino
Breadboard
USB Cable
1 Neo Pixel Strip with 8 LEDs
1 1000F Capacitor
1 10K Ohm resistor
3 Male-Female wires
9 Male-Male wires

## Slide 31: Step 1 – Wire the Rails
Make sure the USB Cable is not plugged into the PC
Run a wire from GND pin on Arduino to blue row on breadboard (green wire in example)
Run a wire from 5V pin on Arduino to red row on breadboard (red wire in example)
Run a wire from pin 5 of the Arduino to I:2 (blue wire in example)

## Slide 32: Step 2 – Wire the LED Strip
Run a wire from the Blue Row on breadboard to the GND pin of the LED strip (green wire in example)
Run a wire from the Red Row on breadboard to the 5V pin of the LED strip (red wire in example)
Run a wire from C:2 to the DIn pin of the LED strip (blue wire in example)

## Slide 33: Step 3 – Wire One Side of Button
Run a wire from the Red Row on breadboard to J:13
Run a wire from the Red Row on breadboard to J:17
Run a wire from the Red Row on breadboard to J:21

## Slide 34: Step 4 – Wire Other Side of Button
Run a wire from pin 11 of the Arudino to J:15
Run a wire from pin 12 of the Arudino to J:19
Run a wire from pin 13 of the Arudino to J:23

## Slide 35: Step 5 – Button Placement
Place the 3 buttons
  One in F:13 and F:15
  One in F:17 and F:19
  One in F:21 and F:23

## Slide 36: Step 6 – Components
Place the Resistor over the gap on F:2 and D:2
Place the capacitor with the long leg in the Red Row and the short leg in the Blue Row

## Slide 37: Step 7 – Power the Arduino
Plug the Arduino into the USB Cable
Plug the USB Cable into the PC

## Slide 38: Step 8 – Program the Arduino
Open Sketch button_driven_led.ino in the button_drive_led directory/folder
Select Tools -> Port
Click the Upload Button

## Slide 39: What Next?
Guided Learning in Kits / Books
Online Tools
  Spark Fun - https://www.sparkfun.com/
What you can do when you got it all down: https://youtu.be/ahpPqD7Ju5w?t=17s