## Slide 1: Maker Camp Arduino
Nancy Rochford, Becky Oberhauser, Ryan Brock

## Slide 2
Hardware

## Slide 3: Software

## Slide 4: The Arduino Uno

## Slide 5: The Arduino Family

## Slide 8: Breadboard
Where is C:19?

## Slide 9: Just Like Battleship

## Slide 10: Be careful to use the correct resistor!

## Slide 11
Guide sections have lots of help

## Slide 12
Begin Circuit 1!
15 Minutes

## Slide 13: Alterations
Turn the LED around so the longer pin is in C2 instead of C3 (then switch it back)
Alter the time the LED is on and off so that is on for 3 seconds and off for ½ second
Change the pin from pin 13 to pin 2
Use 2 330 Ω resistors in place of the 10K Ω resistor
Replace the 2 330 Ω resistors with a single 10K Ω resistor
Alter the program so that the LED blinks on and off for 1 second, then 2 seconds, then 3 seconds, then 4, then 5, then repeats starting with 1 second

## Slide 14: Circuit 1 lessons
A program is called a “sketch”
A sketch:
  contains setup() area
  contains loop() area
  uses “/* */” or “//” for comments
  uses “;” to separate instructions
Commands used:
  pinMode(13, OUTPUT);
  digitalWrite(13, HIGH);
  delay(1000);

## Slide 15: Circuit 1 lessons
Higher Resistance reduces the LED brightness
The ‘D’ in LED stands for diode which means current can only travel in one direction

## Slide 16: Circuit 1 questions
Why do we need the resistors in series with the LED?
What happens each time we add a new one in series or swap it with a much higher resistance?
What would happen if we moved the code from loop() and put it all into setup()?
Did anyone use a loop to modify the program for the last alteration?

## Slide 17: Why is one lead longer?

## Slide 18
Begin Circuit 2!
15 Minutes

## Slide 19: Measurement
Use the multi-meter to read the voltage and resistance across the potentiometer

## Slide 20: Circuit 2 lessons
Arduino has digital and analog pins
Commands used:
  analogRead(sensorPin);
Variable resistance LED brightness

## Slide 21: Circuit 2 questions
Can you describe the difference between the digital and analog pins?
What else can we do with the potentiometer?

## Slide 22: Voltage Division

## Slide 23: Voltage Division
Assume
Vin = 5V
R1 = 100 Ohms
R2 Range is 0 to 100 Ohms

## Slide 24: Uses of Potentiometers and Variable Resistance Components

## Slide 25
Begin Circuit 3!
20 Minutes

## Slide 26: Alterations
Drive all three pins and then use different resistors to adjust the brightness and/or color of the LED
Use a potentiometer to adjust the brightness
Use a potentiometer to adjust the color

## Slide 27: Potentiometer Configuration

## Slide 28: Circuit 3 lessons
All visible color can be generated with three colors, red, green, and blue (RGB)
The colors can be generated by adjusting the brightness of each color
The Arduino can adjust the brightness by using a PWM to drive the pins and simulate varying voltages between 0 and 5V

## Slide 29: Circuit 3 questions
What is the duty cycle of a PWM?
Can you explain the difference between duty cycle and frequency?
How do you make the color purple with an RGB LED?

## Slide 30: PWM

## Slide 31: Monitor/TV/Display Pixels

## Slide 32
Begin Circuit 9!
15 Minutes

## Slide 33: Alterations
Play Mary Had a Little Lamb
EDCDEEE DDD EGG EDCDEEEEDDEDC
Make the speaker sound like a police siren
Add a potentiometer to adjust the frequency

## Slide 34: Potentiometer Configuration

## Slide 35: Circuit 9 lessons
The piezo has the ability to play different frequencies
The Arduino can generate frequencies from 31 to 65535
The piezo in the kit can generate frequencies up to 2048 Hz
The arduino can generate the frequencies using:
tone(pin, frequency)

## Slide 36: Circuit 9 questions
How does a piezo work?
What do you think the Arduino is doing in order to generate the various frequencies?

## Slide 37: Piezoelectric Components

## Slide 38: Frequency or Duty Cycle?

## Slide 39
Begin Circuit 10!
15 Minutes

## Slide 40: Alterations
Add a potentiometer rather than using the Serial input

## Slide 41: Potentiometer Configuration

## Slide 42: Circuit 10 lessons
Transistors allow the Arduino to drive a higher current device like a motor
Transistors act like a digital switch
We can control the DC motor using the Arduino’s PWM

## Slide 43: Circuit 10 questions
What is a diode?
Why is it used in the circuit?
How might we change the motor’s direction?

## Slide 44: DC Motors

## Slide 45: Transistors

## Slide 46: Digital Logic
AND gate
OR gate

## Slide 47: H-Bridge

## Slide 48: Code Alterations
https://github.com/borq79/Cary-Area-Public-Library-Classes/tree/master/courses/arduino_maker_camp_day