## Slide 1: DIY weather station
Session 1 of 5
Cary area public library

## Slide 2: introduction
Ryan Brock
Software Engineer – 15 Years
Purdue University – Computer Science
Motorola
Zebra Technologies

## Slide 3: contact
Twitter: @borq79
Email: borq79@gmail.com
Github Repo: https://github.com/borq79/Cary-Area-Public-Library-Classes
Google Discussion Group: https://groups.google.com/forum/#!forum/cary-area-computer-science-education

## Slide 4: goals
Learn how to program the NodeMCU
Learn how to monitor temperature, humidity, pressure, and light intensity
Learn how to create and read a schematic
Learn how to wire up (solder) components on a PCB
Learn how to integrate components and sensors into a single application
Build a functional weather station that can be monitored from the internet

## Slide 5: Course plan
Day 1 – January 5th
  Introduction
  Safety Overview
  Configure NodeMCU modules
  Thingspeak accounts
Day 2 – January 19th
  Schematics
  Breadboard wire up Test
Day 3 – February 2nd
  How to solder
  Solder up BMP280
  DC Socket Assembly
Day 4 – February 16th
  PCB Assembly
Day 5 – March 2nd
  Final assembly and test
  Review

## Slide 6: Hazards and Warnings
Drilling
Sharp metal edges
Electricity
Solder
Soldering Iron
EYE PROTECTION REQUIRED

## Slide 7: soldering
Be very cautious
300o F to 900o F!
Melt and Fuse Metal
Assume entire rod is hot!
Assume it is always on

## Slide 8: Breadboards
Power and ground rows
Columns are connected
Two sides – Gap separated
Grid Layout
Can you Find C:19?

## Slide 9: Printed Circuit Boards (PCB)
Similar to breadboard grid layout
Columns are NOT connected
Prototyping
Solder to copper pads

## Slide 10: Parts List
Altoids Tin
51K resistor
Photoresistor
DC jack
NodeMCU
BMP280 + Header
3 Female Headers (1 4-pin, 2 15-pin)
5x7 PCB
8 Standoffs
9V Battery Plug
9V Wall Plug

## Slide 11: Resistors
Restrict current
Give off heat
Color bands indicate resistance

## Slide 12: PhotoResistors
Change resistance based on light intensity
Voltage division

## Slide 13: Voltage Division
Vout = (R2 ÷ (R1 + R2)) * Vin

## Slide 14: BMP280 Sensor
Vin – 1.8V – 5V
SCL/SDA – i2c or SPI
Temperature
Humidity
Barometric Pressure

## Slide 15: NodeMCU
ESP8266 - ESP-12E
Version 2
Lua Programming Language
3.3V Based
1 Analog Pin
GPIO and PWMs
Input Voltage 5-10V

## Slide 16: IDE for NodeMCU
Click ESPlorer icon on the desktop

## Slide 17: Flashing Firmware
esptool.py

## Slide 18: Thingspeak
IoT Analytics
Collect and View Data
Free for our usage

## Slide 19: Create thingspeak account
https://thingspeak.com/
Sign Up
Create Account
Create Test Channel
Add single field called ’sample’

## Slide 20: Test MCU
Open mcu_test.lua on desktop under diyweather folder
Change the API key for thinkspeak to your API key
Connect the NodeMCU via USB
Select the Port
Click Open
Click ‘RST’ on the NodeMCU
Click on ‘Save to ESP’

## Slide 21: Next session
January 19th – 5-6:30 pm
Please bring a USB cable for the NodeMCU if you have one
Schematics and Wiring