## Slide 1: DIY weather station
Session 1 of 5
Cary area public library

## Slide 2: introduction
Ryan Brock
Software Engineer – 15 Years
Purdue University – Computer Science
Motorola
Zebra Technologies

## Slide 3: contact
Twitter: @borq79
Email: borq79@gmail.com
Github Repo: https://github.com/borq79/Cary-Area-Public-Library-Classes
Google Discussion Group: https://groups.google.com/forum/#!forum/cary-area-computer-science-education

## Slide 4: goals
Learn how to program the NodeMCU
Learn how to monitor temperature, humidity, pressure, and light intensity
Learn how to create and read a schematic
Learn how to wire up (solder) components on a PCB
Learn how to integrate components and sensors into a single application
Build a functional weather station that can be monitored from the internet

## Slide 5: Course plan
Day 1 – January 5th
  Introduction
  Safety Overview
  Configure NodeMCU modules
  Thingspeak accounts
Day 2 – January 19th
  Schematics
  Breadboard wire up Test
Day 3 – February 2nd
  How to solder
  Solder up BMP280
  DC Socket Assembly
Day 4 – February 16th
  PCB Assembly
Day 5 – March 2nd
  Final assembly and test
  Review

## Slide 6: Hazards and Warnings
Drilling
Sharp metal edges
Electricity
Solder
Soldering Iron
EYE PROTECTION REQUIRED

## Slide 7: soldering
Be very cautious
300o F to 900o F!
Melt and Fuse Metal
Assume entire rod is hot!
Assume it is always on

## Slide 8: Breadboards
Power and ground rows
Columns are connected
Two sides – Gap separated
Grid Layout
Can you Find C:19?

## Slide 9: Printed Circuit Boards (PCB)
Similar to breadboard grid layout
Columns are NOT connected
Prototyping
Solder to copper pads

## Slide 10: Parts List
Altoids Tin
51K resistor
Photoresistor
DC jack
NodeMCU
BMP280 + Header
3 Female Headers (1 4-pin, 2 15-pin)
5x7 PCB
8 Standoffs
9V Battery Plug
9V Wall Plug

## Slide 11: Resistors
Restrict current
Give off heat
Color bands indicate resistance

## Slide 12: PhotoResistors
Change resistance based on light intensity
Voltage division

## Slide 13: Voltage Division
Vout = (R2 ÷ (R1 + R2)) * Vin

## Slide 14: BMP280 Sensor
Vin – 1.8V – 5V
SCL/SDA – i2c or SPI
Temperature
Humidity
Barometric Pressure

## Slide 15: NodeMCU
ESP8266 - ESP-12E
Version 2
Lua Programming Language
3.3V Based
1 Analog Pin
GPIO and PWMs
Input Voltage 5-10V

## Slide 16: IDE for NodeMCU

## Slide 17: Flashing Firmware

## Slide 18: Thingspeak
IoT Analytics
Collect and View Data
Free for our usage

## Slide 19: Create thingspeak account
https://thingspeak.com/
Sign Up
Create Account
Create Test Channel
Add single field called ’sample’

## Slide 20: Test MCU

## Slide 21: Next session
January 19th – 5-6:30 pm
Please bring a USB cable for the NodeMCU if you have one
Schematics and Wiring