## Slide 1: DIY weather station
Session 1 of 5
Cary area public library

## Slide 2: introduction
Ryan Brock
Software Engineer – 15 Years
Purdue University – Computer Science
Motorola
Zebra Technologies

## Slide 3: contact
Twitter: @borq79
Email: borq79@gmail.com
Github Repo: https://github.com/borq79/Cary-Area-Public-Library-Classes
Google Discussion Group: https://groups.google.com/forum/#!forum/cary-area-computer-science-education

## Slide 4: goals
Learn how to program the NodeMCU
Learn how to monitor temperature, humidity, pressure, and light intensity
Learn how to create and read a schematic
Learn how to wire up (solder) components on a PCB
Learn how to integrate components and sensors into a single application
Build a functional weather station that can be monitored from the internet

## Slide 5: Course plan
Day 1 – January 5th
  Introduction
  Safety Overview
  How to Solder
  Solder up BME/BMP280
Day 2 – January 19th
  Schematics
  Breadboard wire up Test
  Configure NodeMCU modules
  Thingspeak accounts
Day 3 – February 2nd
  How to solder review
  DC Socket Assembly
  Solder headers
Day 4 – February 16th
  PCB wiring
Day 5 – March 2nd
  Final assembly and test
  Review

## Slide 6: The Weather station
Runs on 9V
Wall or battery powered
Light, temp, humidity, and pressure
Wifi enabled
Sends data to thingspeak
Hosts web server for configuration

## Slide 7: Hazards and Warnings
Drilling
Sharp metal edges
Electricity
Solder
Soldering Iron
EYE PROTECTION REQUIRED

## Slide 8: soldering
Be very cautious
300o F to 900o F!
Melt and Fuse Metal
Assume entire rod is hot!
Assume it is always on

## Slide 9: Breadboards
Power and ground rows
Columns are connected
Two sides – Gap separated
Grid Layout
Can you Find C:19?

## Slide 10: Printed Circuit Boards (PCB)
Similar to breadboard grid layout
Columns are NOT connected
Prototyping
Solder to copper pads

## Slide 11: Parts List
Altoids Tin
51K resistor
Photoresistor
DC jack
NodeMCU
BME/BMP280 + Header
3 Female Headers (1 4-pin, 2 15-pin)
5x7 PCB
8 Standoffs
9V Battery Plug
9V Wall Plug

## Slide 12: Resistors
Restrict current
Give off heat
Color bands indicate resistance

## Slide 13: PhotoResistors
Change resistance based on light intensity
Voltage division

## Slide 14: Voltage Division
Vout = (R2 ÷ (R1 + R2)) * Vin

## Slide 15: BME/BMP280 Sensor
Vin – 1.8V – 5V
SCL/SDA – i2c or SPI
Temperature
Humidity
Barometric Pressure

## Slide 16: NodeMCU
ESP8266 - ESP-12E
Version 2
Lua Programming Language
3.3V Based
1 Analog Pin
GPIO and PWMs
Input Voltage 5-10V

## Slide 17: How To Solder
Tin the tip
Images courtesy of Adafriut

## Slide 18: How To Solder
Heat the Joint
Images courtesy of Adafriut

## Slide 19: How To Solder
Apply the solder
Images courtesy of Adafriut

## Slide 20: How To Solder
Let it flow
Let it cool
Images courtesy of Adafriut

## Slide 21: How To Solder
Trim the lead
Images courtesy of Adafriut

## Slide 22: Trouble Joints
Cold Joints
Insufficient Wetting
Too Much Solder
Images courtesy of Adafriut

## Slide 23: BME/BMP280 Header Attachment

## Slide 24: Wire Up BME/BMP280 for TEst
GND to A:13 (VIN)
3.3V to A14 (GND)
A5 to A:15 (SCL)
A4 To A:16 (SDA)

## Slide 25: Program Arduino
Go to Sketch -> Include Library -> Manage Libraries
Search for BME
Choose the sparkfun BME280
Open bme280test.ino on the Desktop

## Slide 26: Homework
https://thingspeak.com/
Sign Up
Create Account
Create Test Channel
Add single field called ’sample’

## Slide 27: Next session
January 19th – 5-6:30 pm
Please bring a USB cable for the NodeMCU if you have one
Bring your own soldering iron and safety goggles if you have them
Schematics and Wiring