## Slide 1: DIY Electronics: The Game of Simon using the Arudino
Ryan Brock

## Slide 2: About Me
Ryan Brock
Software Engineer – 14 Years
Purdue University – Computer Science
Motorola
Zebra Technologies

## Slide 3: Contact
Twitter: @borq79
Email: borq79@gmail.com
Github Repo:
  https://github.com/borq79/Cary-Area-Public-Library-Classes

## Slide 4: Agenda
Intro
Wire up Project
Arduino Sketch Basics
WS2811
Buttons and Pullup Resistors
Piezo and tone()
Game Time!

## Slide 5: Your Kits
$55 Vilros Ultimate Starter Kit
https://www.vilros.com/ultimate-starter-kit.html
$8 LED Strip
http://www.amazon.com/NulSom-NeoPixel-Rainbow-Stick-Arduino/dp/B00PTEP14W/ref=sr_1_1?ie=UTF8&qid=1452991973&sr=8-1&keywords=neopixel+stick
$3 20 pc. Capacitor Pack
http://www.dx.com/p/16v-1000uf-aluminum-motherboard-capacitors-20-piece-pack-127865#.V0IQv5MrJMM
50 Button Pack
https://www.amazon.com/gp/product/B00R17XUFC/ref=oh_aui_search_detailpage?ie=UTF8&psc=1

## Slide 6: The Arduino Uno

## Slide 7: Breadboard
Where is C:19?

## Slide 8: Just Like Battleship

## Slide 9: Wiring up a Circuit

## Slide 10: Project Parts List
Arduino
Breadboard
USB Cable
1 Neo Pixel Strip with 8 LEDs
1 1000F Capacitor
1 10K Ohm resistor
3 Male-Female wires
12 Short Male-Male wires
4 small buttons (not the bigger ones)
1 Piezo Speaker

## Slide 11: Step 1 – Place the Buttons and Speaker
Make sure the USB Cable is not plugged into the PC
Place the four buttons – Place the upper left corners in E:25, E:20, E:15, and E:10
Place the Piezo so that the + is in E:3 and the – is in E:1 (the piezo you have will not look like the diagram – it will sit directly on the board)

## Slide 12: Step 2 – Place WS2811 Components
Place the + (longer leg) of the capacitor into the top red row
Place the shorter leg of the capacitor (also the side painted gray) in the top blue row
Place the one leg of the resistor in E:30 and the other leg into G:30

## Slide 13: Step 3 – Start to Wire Up WS2811
Attach the female end of a female-male wire onto the 5V pin of the WS2811 – attach the male end into the 5V of the Arduino
Attach the female end of a female-male wire onto the DIn pin of the WS2811 – attach the male end into the I:30 of the Breadboard

## Slide 14: Step 4 – Run the Ground Wires
Run a wire from GND on the lower row of the Arduino to anywhere in the top blue row
Attach the female end of a female-male wire onto the GND pin of the WS2811 – place the male end into anywhere on the top blue row
Run 5 wires from anywhere on the top blue row to A:25, A:20, A:15, A:10, and A:1

## Slide 15: Step 5 – Run the Data Lines
Run a wire from pin 2 on the Arduino to A:30 (blue wire in diagram)
Run a wire from pin 6 on the Arduino to A:23 (orange wire in diagram)
Run a wire from pin 8 on the Arduino to A:18 (orange wire in diagram)
Run a wire from pin 10 on the Arduino to A:13 (orange wire in diagram)
Run a wire from pin 12 on the Arduino to A:8 (orange wire in diagram)
Run a wire from pin 13 on the Arduino to A:3 (magenta wire in diagram)

## Slide 16: Step 5 – Power on the Arduino
Plug the Arduino into the USB Cable
Plug the USB Cable into the PC

## Slide 17: Step 6 – Program the Arduino
Plug the board into the PC via the USB plug
Open Sketch simon_step_01.ino in the simon_step_01 directory/folder
Select Tools -> Port
Click the Upload Button

## Slide 18: Step 7 – Open the Serial Monitor
Go to Tools and select ‘Serial Monitor’

## Slide 19: WS2811

## Slide 20: Button as a Switch

## Slide 21: Resistors and Pull Up Resistors

## Slide 22: Simon Step 2

## Slide 23: Program the Arduino
Plug the board into the PC via the USB plug
Open Sketch simon_step_02.ino in the simon_step_02 directory/folder
Select Tools -> Port
Click the Upload Button

## Slide 24: Simon Step 3

## Slide 25: Program the Arduino
Plug the board into the PC via the USB plug
Open Sketch simon_step_03.ino in the simon_step_03 directory/folder
Select Tools -> Port
Click the Upload Button

## Slide 26: Simon Step 4

## Slide 27: Piezoelectric Components

## Slide 28: Program the Arduino
Plug the board into the PC via the USB plug
Open Sketch simon_step_04.ino in the simon_step_04 directory/folder
Select Tools -> Port
Click the Upload Button

## Slide 29: Simon Step 5

## Slide 30: Program the Arduino
Plug the board into the PC via the USB plug
Open Sketch simon_step_05.ino in the simon_step_05 directory/folder
Select Tools -> Port
Click the Upload Button