## Slide 1: Arduino Weather Indicator
Ryan Brock

## Slide 2: About Me
Ryan Brock
Software Engineer – 14 Years
Purdue University – Computer Science
Motorola
Zebra Technologies

## Slide 3: Contact
Twitter: @borq79
Email: borq79@gmail.com
Github Repo:
  https://github.com/borq79/Cary-Area-Public-Library-Classes

## Slide 4: Agenda
Review (20 mins)
  Arduino
  Breadboards
  Resistors
  LEDs
  Capacitors
  NeoPixel LED Arrays
  Color
Introduction to the Ethernet Shield and Web APIs (30 mins)
  Networking Terms
  Shield – Getting Connected
  HTTP/REST
  Getting the Weather Conditions
Projects
  Weather Monitor

## Slide 5: Arduino Uno

## Slide 6: Breadboard

## Slide 7: Wiring up a Circuit

## Slide 8: Resistors

## Slide 9: Vilros Kit Resistors
V = IR
I = V / R
I = 5V / 330 = 0.015A (15 mA)
I = 5V / 10,000 = 0.0005A (0.5 mA)

## Slide 10: LEDs

## Slide 11: Why is one lead longer?

## Slide 12: Capacitors

## Slide 13: Charging up a Capacitor
Image from: https://learn.sparkfun.com/tutorials/capacitors

## Slide 14: Adafruit NeoPixel
The Magic of NeoPixels:
https://learn.adafruit.com/adafruit-neopixel-uberguide/
https://www.youtube.com/watch?time_continue=41&v=HO6xQMR8naw

## Slide 15: WS2811

## Slide 16: WS2811
Datasheet: https://www.adafruit.com/datasheets/WS2811.pdf
A ‘chain’ if 24-bit color sequences
Each pixel’s WS2811 IC will program itself and send the rest of the chain down the line

## Slide 17: 24, and 32-bit Color
3 LEDs – Red, Blue, and Green
8-bits for each pixel
0 – 255 different brightness levels for each pixel

## Slide 18: 24, and 32-bit Color
Three colors mix to create 224 (16,777,216) color combinations, or 24-bit color
32-bit color includes transparency, but ignored for NeoPixels

## Slide 19: Powering the Strip
Sources: https://learn.adafruit.com/adafruit-neopixel-uberguide/basic-connections

## Slide 20: Adafruit NeoPixel Library
Go to: https://learn.adafruit.com/adafruit-neopixel-uberguide/arduino-library-installation
Download the library (big green button)
Uncompress the ZIP file
Create a directory named WS2811 in c:\Program Files\Arduino\Libraries
Copy Adafruit_NeoPixel.cpp and Adafruit_NeoPixel.h
Re-Start the Arduino IDE

## Slide 21: Initialization
// Parameter 1 = number of pixels in strip
// Parameter 2 = pin number (most are valid)
// Parameter 3 = pixel type flags, add together as needed:
// NEO_KHZ800 800 KHz bitstream (most NeoPixel products w/WS2812 LEDs)
// NEO_KHZ400 400 KHz (classic 'v1' (not v2) FLORA pixels, WS2811 drivers)
// NEO_GRB Pixels are wired for GRB bitstream (most NeoPixel products)
// NEO_RGB Pixels are wired for RGB bitstream (v1 FLORA pixels, not v2)
Adafruit_NeoPixel strip = Adafruit_NeoPixel(60, PIN, NEO_GRB + NEO_KHZ800);
void setup() {
strip.begin();
strip.show(); // Initialize all pixels to 'off'
}

## Slide 22: Set a Pixel’s Color
// Set each color component individually
strip.setPixelColor(n, red, green, blue);
// Set via 32-bit (24-bit) color
strip.setPixelColor(n, color);
// Don’t forget to ’refresh’ the pixel
strip.show();

## Slide 23: Ethernet Shield
W5100 with internal 16K buffer
Connection speed: 10/100Mb
Onboard SD card slot
Connection with Arduino on SPI port

## Slide 24: Some Networking Terms
Ethernet
Protocols
MAC Address
TCP, UDP, IP
DHCP vs. Static
Port (80, 443)
Ping
HTTP

## Slide 25: Networking OSI Model

## Slide 26: Connect to a Network
https://www.arduino.cc/en/Tutorial/WebClient
// Ethernet Shield Information
#define ETHERNET_SHIELD_MAC {0xDE, 0xAD, 0xBE, 0xEF, 0x00, 0x00}
byte ethernetMACAddress[] = ETHERNET_SHIELD_MAC;
EthernetClient client;
// Initialize the shield
Ethernet.begin(ethernetMACAddress);
// print out the IP address
Serial.print("IP = "); Serial.println(Ethernet.localIP());
// Connect to the server
client.connect("www.google.com", 80);
// Send the HTTP request to get the HTML response
client.println("GET /search?q=arduino HTTP/1.1"); client.println("Host: www.google.com"); client.println("Connection: close");
// While data is available, read the response and print it out
if (client.available()) { char c = client.read(); Serial.print(c); }
// Finish
client.stop();

## Slide 27: HTTP / REST / JSON / XML
HTTP (Hypertext Transfer Protocol)
  GET / POST / PUT / DELETE
  200, 404, 500
API (Application Programming Interface)
ReST (Representational State Transfer)
  Send HTTP request
  HTML, JSON, XML response

## Slide 28: HTTP / REST / JSON / XML
HTTP GET Example – Search Google
GET /search?q=arduino HTTP/1.1 Host: www.google.com Connection: close
\r\n
Response 200 OK

## Slide 29: HTML
<html>
<head>
<title> response </title> </head>
<body>
A = 1 <br/>
B = 2 <br/>
C = 3 <br/>
</body>
</html>

## Slide 30: JSON
{
“A”: “1”,
“B”: “2”,
”C”: “3”
}

## Slide 31: XML
<xml>
<document>
<items>
<item name=“A”>1</item>
      <item name=“B”>2</item>
      <item name=“C”>3</item>
</items>
</document>
</xml>

## Slide 32: Get the Weather
‘Screen Scrape’ weather.com
Weather Underground API
Temboo Reduced Response API

## Slide 33: Temboo
Code Generation
Easy API
Library Provided
Sign up for an account to get a development key
https://temboo.com/library/Library/Yahoo/Weather/GetWeatherByAddress/
Yahoo Weather Conditions
https://gist.github.com/bzerangue/805520

## Slide 34: Project Parts List
Arduino
Breadboard
USB Cable
Ethernet Shield
Ethernet Cable (provided by Ryan)
1 Neo Pixel Strip with 8 LEDs
1 1000F Capacitor (provided by Ryan)
1 10K Ohm resistor (in kit)
3 Male-Female wires (provided by Ryan)
3 Male-Male wires (in kit)

## Slide 35: Project Wiring Diagram

## Slide 36: Project Wiring Photo

## Slide 37: Project One Code
https://github.com/borq79/Cary-Area-Public-Library-Classes
  weather
    weather_meter
      weather_meter.ino